## Slide 1
Programming Foundations
Level 1

## Slide 2
2
Programming Foundations
Level 1
Binary System

## Slide 3
Understanding the Binary System in Computers
Computers are electronic devices that work entirely using electricity — signals that are either ON or OFF.
Because of this, they can only understand two states: 1 (ON) and 0 (OFF).
This fundamental concept is the basis of everything a computer does — numbers, letters, images, and sounds are all represented in binary form.
Understanding the binary system is the first step toward mastering computer logic and programming.

## Slide 4
How Computer Works?
🟨 A computer processes information using electrical signals.
🟨 It understands only 0s and 1s (binary digits).
🟨 These digits represent electrical states — Off (0) or On (1).
🟨 Billions of these tiny electrical switches called transistors form the CPU and handle all computations.
🟨 Inside the CPU (Central Processing Unit), there are hundreds of millions — or even billions — of transistors.
🟨 A transistor is a microscopic binary switch that either allows or blocks the flow of electricity.
🟨 Every calculation, text, sound, or image you see on your screen is made possible by these transistors switching ON and OFF billions of times per second.
💡 Example: When you press a key on your keyboard, your CPU processes the electrical signal (a pattern of 0s and 1s) to decide what to display.

## Slide 5
How Computer Works?
🟨 Computer is an electronic device.
🟨 It deals with electricity On/Off
🟨 It only understands 0’s (Off) and 1’s (On).
🟨 Everything you see, hear and read on the screen reaches you as the result of “on” or “off” billions of times.
🟨 Computer uses Binary System to represent numbers, letters, commands, images and sounds.

## Slide 6
2
Programming Foundations
Level 1
Binary System

## Slide 7
The Binary System
🟨 The binary system is a base-2 numbering system.
🟨 It uses only two digits: 0 and 1.
🟨 Every binary position represents a power of 2 (1, 2, 4, 8, 16, 32, 64, 128 …).

## Slide 8
Decimal vs Binary?

## Slide 9
2
Programming Foundations
Level 1
What is bit?

## Slide 10
What is Bit?
Remember! .. Computer is an electronic device…it deals with electricity only.
Bit = “Binary Digit” → the smallest piece of information (either 0 or 1).

## Slide 11
2
Programming Foundations
Level 1
What is byte?

## Slide 12
What is Byte?
Byte = group of 8 bits.
Each bit in a byte has a positional value:

## Slide 13
2
Programming Foundations
Level 1
Decimal to Binary

## Slide 14
Converting Between Decimal and Binary
Decimal → Binary:
Divide the decimal number by 2 repeatedly and note the remainders (bottom to top).

## Slide 15
Represent this in binary…

## Slide 16
Represent this in binary…

## Slide 17
Represent this in binary…

## Slide 18
Represent this in binary…

## Slide 19
Represent this in binary…
Only one way to represent Data

## Slide 20
2
Programming Foundations
Level 1
Binary to Decimal

## Slide 21
Converting Between Decimal and Binary
Binary → Decimal:
Multiply each bit by its positional value and add them.

## Slide 22
Represent this in decimal…

## Slide 23
Represent this in decimal…

## Slide 24
Represent this in decimal…

## Slide 25
Represent this in decimal…

## Slide 26
Represent this in decimal…

## Slide 27
“Only One Way” to Represent a Number in Binary
In binary, every non-negative integer has exactly one representation (if you ignore leading zeros).
This means there is one unique set of bits (MSB…LSB) whose weighted sum equals the number.
You cannot choose a different combination of bit positions to get the same number — each power of two (1, 2, 4, 8, 16, …) is either used once or not used.
So in the above example the number 20 only comes from 4 + 16 bits, while in decimal system 20 can come from 10 + 10 , or 18 + 2 , or 15 + 5 ...etc.

## Slide 28
2
Programming Foundations
Level 1
Capacity of Byte

## Slide 29
What is the largest number in byte?
1 byte = 8 bits → max number = 255 (11111111).

## Slide 30
What if I have larger number such as 257?!!
2 bytes = 16 bits → max number = 65,535 (1111111111111111).

## Slide 31
Represent this in binary…

## Slide 32
What is the largest number in 2 bytes?

## Slide 33
But!
How to represent letters?

## Slide 34
2
Programming Foundations
Level 1
ASCII & Unicode

## Slide 35
Representing Characters – ASCII
🟨 Computers use codes to represent letters and symbols.
🟨 ASCII (American Standard Code for Information Interchange) assigns a unique binary code to each character.
💡 Example:
  🟩 ‘A’ = 65 = 01000001
  🟩 ‘B’ = 66 = 01000010
  🟩 Space = 32 = 00100000
🟨 Limitation: ASCII supports only English letters and limited symbols (128 or 256 codes).

## Slide 37
How to represent letters?

## Slide 38
This is my name in binary:
Sara Alterkawi
01010011 01100001 01110010 01100001 00100000 01000001 01101100 01110100 01100101 01110010 01101011 01100001 01110111 01101001

## Slide 39
What does this mean?
01001001 00100000 01001100 01101111 01110110 01100101 00100000 01011001 01101111 01110101 00100001

## Slide 40
But!
How to represent Arabic letters?

## Slide 41
2
Programming Foundations
Level 1
Unicode

## Slide 42
Representing Characters – ASCII
🟨 To represent all world languages, Unicode was developed.
🟨 Unicode supports:
  🟩 UTF-8 → 256 characters
  🟩 UTF-16 → 65,536 characters
  🟩 UTF-32 → 4,294,967,296 characters
💡 Example:
Arabic letters such as “ساره” require Unicode because ASCII cannot represent them.

## Slide 44
Problem:

## Slide 46
ASCII
VS
UNICODE
American Standard Code for Information Interchange
Supports specific characters (less space)
Has 2 standards:
bit ASCII – 128 characters
bit ASCII – 256 characters
Only one language
Universal Coding System
rge number of characters (large space)
It has 3 standards:
UTF 8 – 256 characters
UTF 16 – 65,536 characters
UTF 32 – 4,294,967,296 characters
Any combination of languages
Diffrences

## Slide 47
2
Programming Foundations
Level 1
Largest number in Binary System

## Slide 49
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
32,768 | 16,384 | 8,192 | 4,096 | 2,048 | 1,024 | 512 | 256
8,388,608 | 4,194,304 | 2,097,152 | 1,048,576 | 524,288 | 262,144 | 131,072 | 65,536
2,147,483,648 | 1,073,741,824 | 536,870,912 | 268,435,456 | 134,217,728 | 67,108,864 | 33,554,432 | 16,777,216
5.49756E+11 | 2.74878E+11 | 1.37439E+11 | 68,719,476,736 | 34,359,738,368 | 17,179,869,184 | 8,589,934,592 | 4,294,967,296
?? |  |  |  |  |  |  | 

## Slide 50
8 bytes (64 bits) → Value on 64th square =
9,223,372,036,854,775,808.

## Slide 51
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
32,768 | 16,384 | 8,192 | 4,096 | 2,048 | 1,024 | 512 | 256
8,388,608 | 4,194,304 | 2,097,152 | 1,048,576 | 524,288 | 262,144 | 131,072 | 65,536
2,147,483,648 | 1,073,741,824 | 536,870,912 | 268,435,456 | 134,217,728 | 67,108,864 | 33,554,432 | 16,777,216
5.49756E+11 | 2.74878E+11 | 1.37439E+11 | 68,719,476,736 | 34,359,738,368 | 17,179,869,184 | 8,589,934,592 | 4,294,967,296
?? |  |  |  |  |  |  | 

## Slide 52
Total sum (1 to 64) →18,446,744,073,709,600,000

## Slide 53
✨ Summary
✅ Binary System → Foundation for all digital data. ✅ Bits & Bytes → Determine data size and capacity. ✅ ASCII → Enables computers to represent text in English. ✅ Unicode → Expands capability to represent global languages.
By understanding how binary underlies all computer data, you gain insight into how programs, storage, and communication truly work! ⚡

## Slide 54
🧐 Activity
📋 Instructions:
1️⃣ Convert the following decimal numbers into binary:
44
129
512
717
999
2️⃣ Write your first name in binary using ASCII encoding

## Slide 55
🧐 Activity Solution
📋 Solution:
1️⃣ Binary conversions:
🟩 Convert 44 → Binary
Divide 44 by 2:
44 ÷ 2 = 22 remainder 0 22 ÷ 2 = 11 remainder 0 11 ÷ 2 = 5 remainder 1 5 ÷ 2 = 2 remainder 1 2 ÷ 2 = 1 remainder 0 1 ÷ 2 = 0, remainder 1
Now read remainders bottom → top: 1 0 1 1 0 0
➡️ 44 (decimal) = 101100 (binary)

## Slide 56
🧐 Activity Solution
📋 Solution:
1️⃣ Binary conversions:
🟩 Convert 129 → Binary
Divide 129 by 2:
129 ÷ 2 = 64 remainder 1 64 ÷ 2 = 32 remainder 0 32 ÷ 2 = 16 remainder 0 16 ÷ 2 = 8 remainder 0 8 ÷ 2 = 4 remainder 0 4 ÷ 2 = 2 remainder 0
2 ÷ 2 = 1 remainder 0
1 ÷ 2 = 0 remainder 1
Now read remainders bottom → top: 1 0 0 0 0 0 0 1
➡️ 129 (decimal) = 10000001 (binary)

## Slide 57
🧐 Activity Solution
📋 Solution:
1️⃣ Binary conversions:
🟩 Convert 512 → Binary
Divide 512 by 2:
512 ÷ 2 = 256 remainder 0
256 ÷ 2 = 128 remainder 0
128 ÷ 2 = 64 remainder 0 64 ÷ 2 = 32 remainder 0 32 ÷ 2 = 16 remainder 0 16 ÷ 2 = 8 remainder 0 8 ÷ 2 = 4 remainder 0 4 ÷ 2 = 2 remainder 0
2 ÷ 2 = 1 remainder 0
1 ÷ 2 = 0 remainder 1
Now read remainders bottom → top: 1 0 0 0 0 0 0 0 0 0
➡️ 512 (decimal) = 1000000000 (binary)

## Slide 58
🧐 Activity Solution
📋 Solution:
1️⃣ Binary conversions:
🟩 Convert 717 → Binary
Divide 717 by 2:
717 ÷ 2 = 358 remainder 1
358 ÷ 2 = 179 remainder 0
179 ÷ 2 = 44 remainder 1
44 ÷ 2 = 22 remainder 0
22 ÷ 2 = 11 remainder 0
11 ÷ 2 = 5 remainder 1
5 ÷ 2 = 2 remainder 1
2 ÷ 2 = 1 remainder 0
1 ÷ 2 = 0 remainder 1
Now read remainders bottom → top: 1 0 1 0 0 1 1 0 1
➡️ 512 (decimal) = 101001101 (binary)

## Slide 59
🧐 Activity Solution
📋 Solution:
1️⃣ Binary conversions:
🟩 Convert 999 → Binary
Divide 999 by 2:
999 ÷ 2 = 499 remainder 1
499 ÷ 2 = 249 remainder 1
249 ÷ 2 = 124 remainder 1
124 ÷ 2 = 62 remainder 0
62 ÷ 2 = 31 remainder 0
31 ÷ 2 = 15 remainder 1
15 ÷ 2 = 7 remainder 1
7 ÷ 2 = 3 remainder 1
3 ÷ 2 = 1 remainder 1
1 ÷ 2 = 0 remainder 1
Now read remainders bottom → top: 1 1 1 1 1 0 0 1 1 1
➡️ 512 (decimal) = 1111100111 (binary)

## Slide 60
🧐 Activity Solution
📋 Solution:
2️⃣ Example (Name: “Omar”):
🔤 Step 1 — Get the ASCII Codes
Letter ASCII(Decimal)
O 79
m 109
a 97
r 114

## Slide 61
🧐 Activity Solution
📋 Solution:
2️⃣ Example (Name: “Omar”):
🔤 Step 2: Now we convert each decimal value to binary using repeated division:
Convert "O" (79) to Binary
Divide 79 by 2:
79 ÷ 2 = 39 remainder 1 39 ÷ 2 = 19 remainder 1 19 ÷ 2 = 9 remainder 1 9 ÷ 2 = 4 remainder 1 4 ÷ 2 = 2 remainder 0 2 ÷ 2 = 1 remainder 0 1 ÷ 2 = 0 remainder 1
Now read remainders bottom → top:
1 0 0 1 1 1 1
➡️ O = 01001111

## Slide 62
🧐 Activity Solution
📋 Solution:
2️⃣ Example (Name: “Omar”):
🔤 Step 2: Now we convert each decimal value to binary using repeated division:
Convert “m" (109) to Binary
Divide 109 by 2:
109 ÷ 2 = 54 remainder 1 54 ÷ 2 = 27 remainder 0 27 ÷ 2 = 13 remainder 1 13 ÷ 2 = 6 remainder 1 6 ÷ 2 = 3 remainder 0 3 ÷ 2 = 1 remainder 1 1 ÷ 2 = 0 remainder 1
Now read remainders bottom → top:
1 1 0 1 1 0 1
➡️ m = 01101101

## Slide 63
🧐 Activity Solution
📋 Solution:
2️⃣ Example (Name: “Omar”):
🔤 Step 2: Now we convert each decimal value to binary using repeated division:
Convert “a" (97) to Binary
Divide 97 by 2:
97 ÷ 2 = 48 remainder 1 48 ÷ 2 = 24 remainder 0 24 ÷ 2 = 12 remainder 0 12 ÷ 2 = 6 remainder 0 6 ÷ 2 = 3 remainder 0 3 ÷ 2 = 1 remainder 1 1 ÷ 2 = 0 remainder 1
Now read remainders bottom → top:
1 1 0 0 0 0 1
➡️ a = 01100001

## Slide 64
🧐 Activity Solution
📋 Solution:
2️⃣ Example (Name: “Omar”):
🔤 Step 2: Now we convert each decimal value to binary using repeated division:
Convert “r" (114) to Binary
Divide 97 by 2:
114 ÷ 2 = 57 remainder 0 57 ÷ 2 = 28 remainder 1 28 ÷ 2 = 14 remainder 0 14 ÷ 2 = 7 remainder 0 7 ÷ 2 = 3 remainder 1 3 ÷ 2 = 1 remainder 1 1 ÷ 2 = 0 remainder 1
Now read remainders bottom → top:
1 1 1 0 0 1 0
➡️ r = 01110010

## Slide 65
🧐 Activity Solution
📋 Solution:
2️⃣ Example (Name: “Omar”):
➡️ “Omar” = 01001111 01101101 01100001 01110010

## Slide 66
🏁 Conclusion
✅ Binary is the language of computers. Every piece of data — from text to images is built from bits and bytes represented as 0s and 1s.
✅ Understanding binary helps you grasp how information is stored, processed, and communicated inside a computer.
✅ As a foundation in programming, mastering this concept prepares you for deeper topics like data types, memory, and algorithms. 🚀

## Slide 67
Thank you 